## Slide 1: Design Review 1
Team 8
Ze An
Priyanka Anantha
De-Wei Chang
Andria Nyenhuis
Tong Shen

## Slide 2: Function Decomposition
Function decomposition leads to identifying robot attributes
Identify ball
Move to ball
Collect ball
Identify container door
Open container door
Dispense ball
Close container door
Move to container

## Slide 3: Design Overview
Ball identification
  Pixy Smart Vision Detection
Move to ball
  Rear wheel drive, 2x 12V DC motors with 43.7:1 gear box
  Direction control : encoders and Pixy feedback
Ball collection
  Chassis trap container
  Servo motor driven door mechanism
Container door identification
  Pixy Smart Vision Detection
Container door open
Ball dispensing
  Push plate driven by DC motor coupled to lead screw
Container door close

## Slide 4: Subsystem Break Down
Controls
Electronics
Mechanical
ball tracking
motors
FSM
sensors
motors
driver
batteries
microcontroller
chassis
push plate
trap door
wheels
wheel mount
motor mounts
lead screw assembly

## Slide 5: Mechanical Subsystem
Door Closed
Door Open

## Slide 6: Mechanical Subsystem Component Requirements
Chassis
  structural
  resistant to vibrations
  easy to process
  easy to assemble
Push Plate
  light weight
  rigid
Trap Door
  light weight
  rigid
Wheels
  tall
  Traction
  minimal start up torque
Component Mounts
  rigid
  secure method to chassis
Lead Screw Assembly
  robust to misalignment

## Slide 7: Mechanical Subsystem Component Selection
Chassis
  laser cut acrylic sheets
  joined with corner brackets and M3 bolts
Push Plate
  reinforced cardboard
Trap Door
  reinforced cardboard
Wheels
  Front : metal ball casters
  Back : TBD
Component Mounts
  corner brackets and direct mounts
Lead Screw Assembly
  robust to motor coupling misalignment
  DC motor with worm gear

## Slide 8: Mechanical Subsystem Prototype

## Slide 9: THANK YOU